## Slide 1
Solar plant setup for 10 houses

## Slide 2: Problem statement
We have a setup of 10 houses which need solar panels installed
Would it be better to have each house with its own solar panel?
  Considerations: each house needs its own inverter, might not manage the load
Or have a small solar farm which feeds all the houses?
  No load problems per house, if one needs more than
  Less inverters needed
  If solar farm fails, all houses affected
Want to show that a solar farm will be a more beneficial setup due to the higher capacity evening out the load per house even if they exceed a single solar panel capacity

## Slide 3: Setup 1: Solar panel per house
PV profile
[PV Profile]
- profile (map)
PV [Solar Panel] (unit)
- Is_active
- Existing
Battery
[Battery]
(node)
- Is_active
- Has_balance
- Has_storage
- Existing
- Storage_start_end_method
- Storage_state_start
- Storage_state_end
- penalty_down
- penalty_up
DC bus [DC Bus] (node)
- Is_active
- Has_balance
- penalty_up and down
Unit_node_profile
- profile_method: upper_limit
Unit_outputNode
Inverter
[Inverter] (unit)
- Is_active
- Existing
- Efficiency
House / AC bus [House] (node)
- Is_active
- Has_balance
- Inflow
- Penalty_up and penalty_down
Charger/discharger
[Battery Charger]
(connection)
- Is_active
- Existing
- Efficiency
- transfer_method
Connection_node_node
Connection_node_node
Grid [Grid] (node)
- Is_active
Grid supply
[Electricity] (commodity)
- price
Commodity_node
Unit_inputNode
+ If demand response:
- Has_storage
- Existing (constant/time varying)
- Storage_state_Start/end method
House electricity
[Electricity Supply]
(connection)
- Is_active
- Existing
- Efficiency

## Slide 4: Setup 2: Solar grid for all houses
PV units aggregated
[Solar Panel] (unit)
- Is_active
- Existing
Batteries aggregated
- possibility to simulate partial unavailability (to model reliability)
[Battery]
(node)
- Is_active
- Has_balance
- Has_storage
- Existing
- Storage_start_end_method
- Storage_state_start
- Storage_state_end
- penalty_down
- penalty_up
Inverters aggregated
- possibility to simulate partial unavailability (to model reliability)
[Inverter] (unit)
- Is_active
- Existing
- Efficiency
DC buses aggregated [DC Bus] (node)
- Is_active
- Has_balance
- penalty_up and down
Each house as own node with own load profile
AC buses aggregated
[AC Bus] (node)
- Is_active
- Has_balance
- penalty_up and down
PV profile
[PV Profile]
- profile (map)
Unit_node_profile
- profile_method: upper_limit
Grid supply
[Electricity] (commodity)
- price
Grid [Grid] (node)
- Is_active
Unit_outputNode
Unit_inputNode
Connection_node_node
Commodity_node
Connection_node_node
House / AC bus
[House 1, House 2 etc.] (node)
- Is_active
- Has_balance
- Inflow
- Penalty_up and penalty_down
+ If demand response:
- Has_storage
- Existing (constant/time varying)
- Storage_state_Start/end method
Charger/discharger
[Battery Charger]
(connection)
- Is_active
- Existing
- Efficiency
- transfer_method
Electricity Supply
[Grid to AC Bus Supply]
(connection)
- Is_active
- Existing
- Efficiency
Connection_node_node per house
House x Supply per house
[House x Supply]
(connection)
- Is_active
- Existing
- Efficiency

## Slide 6: Setup 2: (deprecated) solar grid per all houses
PV units aggregated
Batteries aggregated
- possibility to simulate partial unavailability (to model reliability)
Inverters aggregated
- possibility to simulate partial unavailability (to model reliability)
DC buses aggregated
Each house as own node with own load profile
Grid connection
AC buses aggregated

## Slide 7: Thank you